## Slide 1: Automated Water Level Monitoring
Team Aqua

## Slide 2: Problem
In day-to-day life when we use motor for pumping water into the over head tank there is high possibility of
Tank overflowing - Water getting wasted
Tank Water Getting Emptied
These problems occur because people cannot accurately switch OFF/ON the motor.

## Slide 3: Solution
When motor is switched on and when the water level reaches an upper limit the microcontroller will sense it and will automatically switches off the motor
Also, when the water level is low, it automatically switches ON the motor.

## Slide 4: Materials Required
Arduino UNO Board
Wi-Fi Module (ESP8266)
Ultrasonic Sensor
Motor Pump
Connecting wires

## Slide 5
BLOCK DIAGRAM
Arduino UNO
Ultrasonic sensor
Tank
Motor pump
Water supply
Voltage regulator(5V)
Wi-Fi
Power supply (220V)
Step down transformer
Rectifier (12V)
Internet

## Slide 6: WORKING
Arduino Uno is connected to an ultrasonic sensor, Wi-Fi module (ESP8266) that processes and transfers recorded data using sensors to the cloud.
Wi-Fi module will trigger the Atmega 328 microcontroller, which will get +5-volt DC supply from the supply voltage.
Stored data is accessed by the user through the web.
This enables the user to check the level of water.
User logs in to the integrated website and set the minimum water level and maximum water level in the tank.
If minimum input water level value is reached, the Motor is turned ON. It begins to fill water in the tank until maximum input water level value is reached in the water tank.
Once the maximum water level value is reached, the motor is turned OFF.

## Slide 7
ARDUINO
SET water level
Check water level
Turn ON the motor
Turn off the motor
Creates a log in the server
Web
Near to minimum
Close to maximum limit

## Slide 8: Budget Estimation
Arduino UNO Board – Rs.1000
Wi-Fi Module (ESP8266) – Rs. 400
Ultrasonic Sensor – Rs. 200
Motor Pump – Rs. 200
Connecting wires and other minimal components – Rs. 200
TOTAL = Rs.2000 (approx.)

## Slide 9
Thank You